## Slide 1: RedMule cube unit in GVSoC
Chi Zhang chizhang@iis.ee.ethz.ch

## Slide 2
Current Progress
Redmule is Ready in GVSoC
  A complete Redmule unit is modeled in GVSoC
  Integrated to Pulp-Cluster in GVSoC
  Redmule Hardware Abstraction Layer(HAL) is ready for SW develpment
Cross-Benchmark
  Compare the runtime of Redmule model in GVSoC and RTL
  The average runtime deviation is 6%
Debugging
  GVSoC’s Redmule doesn’t function correctly when the Matrix dimension can not be divided exactly by Redmule’s dimension

## Slide 3
SW example to use Redmule
Redmule SW flow
  Use one core to interact with Redmule
  Configure Redmule
  Trigger Redmule and wait for finishing
RedMule HAL
  Calculate Metadata for Redmule
  Write to Redmule configure register

## Slide 4
Cross-Benchmark Redmule
Settings
  Benchmark GVSoC model‘s accuracy
  Redmule configure with 12x4 CE arrays
  Varying input matrix dimension
  Compare Redmule runtime cycles
Cross-Benchmark Results
  The average runtime deviation is 6%
  Both RTL & GVSoC models could reach relatively high compute utilization
  At some input matrix dimensions, the runtime deviation goes upto 10%, I need to look in-depth what is happening there.
Chart: Matrix Dimension M-N-K
| 48-64-48 | 48-64-96 | 96-64-48 | 48-128-48 | 48-64-192 | 96-64-96 | 192-64-48 | 48-128-96 | 96-128-48 | 96-64-192 | 192-64-96 | 48-128-192 | 96-128-96 | 192-128-48
GVSoC | 3240 | 6312 | 6334 | 7080 | 12456 | 12456 | 12456 | 13992 | 13992 | 24766 | 24766 | 27838 | 27838 | 27838
RTL | 3152 | 6236 | 6236 | 6224 | 12404 | 12404 | 12404 | 12380 | 12380 | 24740 | 24740 | 24692 | 24692 | 24692
GVSoC-Uti | 94.8148 | 97.3384 | 97.0003 | 86.7797 | 98.6513 | 98.6513 | 98.6513 | 87.8216 | 87.8216 | 99.2328 | 99.2328 | 88.2822 | 88.2822 | 88.2822
RTL-Uti | 97.4619 | 98.5247 | 98.5247 | 98.7147 | 99.0648 | 99.0648 | 99.0648 | 99.2569 | 99.2569 | 99.3371 | 99.3371 | 99.5302 | 99.5302 | 99.5302

## Slide 5
On going work -- Extend to a giant RedMule
Extend to a giant RedMule
  Meet KiloPEs  Configure 48x16 CEs in RedMule
  Extend the BW from TCDM to RedMule
We meet bugs
  Both GVSoC and RTL model trgger bugs when extend CE arrays
  Either the Redmule stall at a point forever or generate incorrect results
Plan for next
  Hopefully we‘ll fix all bugs before next meeting, and cross-benchmark the extended Redmule‘s performance